## Slide 1
Alireza Shafaei, Hassan Afzali-Kusha, and Massoud Pedram
Department of Electrical Engineering
University of Southern California
http://sportlab.usc.edu/
Minimizing the Energy-Delay Product of SRAM Arrays using a Device-Circuit-Architecture Co-Optimization Framework

## Slide 2
1
Introduction
  6T SRAM cell with HVT devices
Read/write-assist techniques
SRAM array model
Simulation results
Conclusion
Outline

## Slide 3
2
Read stability (non-destructive read) requirement:
Write-ability (successful write) requirement:
Can easily fail under process variations
  Sizing up transistors or adopting more robust SRAM cells (e.g., 8T) come at the cost of larger layout area
  Width quantization property in FinFETs
    Ideal case: single-fin devices for all transistors
6T SRAM Cell
PD: Pull-down transistors (M1 and M2)
PU: Pull-up transistors (M3 and M4)
AC: Access transistors (M5 and M6)

## Slide 4
3
All-single-fin 6T SRAM
  Operating at low voltages
    To reduce the power consumption
  Equipped with assist circuits
    To improve degraded stability and performance metrics
Alternative solution: Use high-Vt (HVT) devices in SRAM cells
Devices used in this paper
A 7nm FinFET library under Vdd = 450mV (nominal supply voltage)
  HVT compared with low-Vt (LVT) counterparts have 2 lower ON current, 20 lower OFF current, and 10 higher ON/OFF current ratio.
http://sportlab.usc.edu/downloads/packages/
Area/Power-Efficient SRAMs

## Slide 5
4
Advantages of using HVT devices in SRAM cells:
  Lower OFF current  significant leakage power reduction
  Higher ON/OFF  static noise margin (SNM) improvement
Major drawback:
  Lower ON current  reduces the read current  increases the bitline (BL) delay  performance degradation
6T SRAM with HVT Devices

## Slide 6
5
BL delay can be modeled as follows:
Reduce (sensing voltage):
  Difficult to do due to the increased effect of process variations
Increase (read current):
  By assist circuits. Such circuits are also needed to improve the RSNM and write margin of the all-single-fin 6T SRAM cell.
Decrease (BL capacitance):
  By decreasing (i) the number of rows (or the number of SRAM cells in each column) of the array, and (ii) the number of pre-charger/write buffer transistors
Mitigating the BL Delay

## Slide 7
6
Read-Assist Techniques
Effective in reducing BL delay
Effective in improving RSNM

## Slide 8
7
WL overdrive: VWL is set to a voltage level higher than Vdd to strongly turn on the access transistor.
Negative BL: Write operation into the SRAM cell conventionally (without write-assist) occurs from a BL that is 0. By using a negative voltage for that BL, the gate-to-source voltage becomes larger, more strongly turning on the access transistor.
Write-Assist Techniques

## Slide 9
8
SRAM Array Model
Cell Vdd
Cell Vss

## Slide 10
9
An SRAM array with rows and columns is assumed.
  Capacity: bits
, , and are provided by external sources or on-die DC-DC converters
In each access cycle, bits are read or written
  If , then column decoder/multiplexer are also needed
(): # of fins of pre-charger (write buffer) transistor
SRAM Array Model (2)
(): read (write) access delay
(): read (write) access energy
: ratio of read access to the total access
: array activity factor
: leakage power of an SRAM cell
Tables 1, 2, and 3 in the paper

## Slide 11
10
Given (the capacity of SRAM array in bits)
Find the values of , , , (), , and
Such that is minimized
While yield requirements of SRAM cells are satisfied
Yield constraint:
Optimization Problem
, depending on yield requirements
: the minimum acceptable noise margin level

## Slide 12
11
M1: only one extra voltage level (a high voltage) other than is available, whose value is set to , i.e., 640mV (550mV) for 6T-LVT (6T-HVT).
M2: No restriction on the number of voltage levels is considered. Hence, we have three extra pins for LVT-based array (=640mV, =490mV, and ). However, since and are very close in 6T-HVT, only two pins are used for HVT-based array (= =550mV, and ).
Simulation Setup

## Slide 13
12
Simulation Results: Delay

## Slide 14
13
Simulation Results: Delay

## Slide 15
14
Simulation Results: Energy

## Slide 16
15
Simulation Results: DelayEnergy

## Slide 17
16
By using the proposed optimization framework, for SRAM array capacities ranging from 1KB to 16KB, on average 59% lower energy-delay product with maximum 12% (and on average 9%) performance penalty is achieved.
Conclusion

## Slide 18
Thanks!